## Slide 1
History, Features and Deployment
10/2023 - Stefan Dambeck DC7DS

## Slide 2
How it all began
WebSDR / OpenWebRX History
01
A walk through OpenWebRX(+) features and decoding capabilities
OpenWebRX(+) Features
02
How to roll your own instance of OpenWebRX(+)
OpenWebRX(+) Deployment
03
Hands-on demonstration
OpenWebRX+ Demo
04
Agenda

## Slide 3
WebSDR / OpenWebRX History
How it all began

## Slide 4
History of SDRs and WebSDR
2015
2022
2019
2012
2008
2005
1982
HPSDR
The High Performance SDR project was started in October, 2005 by Phil Covington (N8VB)
First SDR
Developed by Ulrich L. Rohde (N1UL) for the DoD
First WebSDR
Pieter-Tjerk de Boer (PA3FWM) created the first WebSDR at the University of Twente
OpenWebRX+
Marat Fayzullin (no ham radio license) forked and massively extended OpenWebRX into OpenWebRX+
OpenWebRX started
András Retzler (HA7ILM) started OpenWebRX as his BSc thesis
RTL-SDR
Eric Fry discovered that simple DVB-T dongles could be used as a full featured SDR
OpenWebRX revived
Jakob Ketterl (DD5JFK) took over the then stale owrx project and added lots of features and greatly improved SDR support
OpenWebRX 1.2.2 and OpenWebRX+ 1.2.33
Two owrx flavors are available for all relevant platforms (AMD64, arm, arm64) – packages and containers
owrx
owrx+

## Slide 5
WebSDR by PA3FWM

## Slide 6
WebSDR by PA3FWM

## Slide 7
OpenWebRX by HA7ILM
Early OpenWebRX
As of 2016, OpenWebRX had basic features
FM, AM, SSB, CW
Squelch and volume controls
Some waterfall controls
Purely text-based config
Broad SDR support (RTLSDR, Airspy, HPSDR, SDRplay and many more)

## Slide 8
OpenWebRX-Rework by DD5JFK
New OpenWebRX
Jakob DD5JFK greatly enhanced the features of OpenWebRX
Config Web-Gui
Digital Voice (D-Star, C4FM, DMR, NXDN) and Digimode (APRS, FT8/4, WSPR, JS8) decoders integrated into web-ui
Bookmarks and labels
Map view showing decoded signals and their origin (FT8/4, WSPR, JS8, APRS)
Background decoding
Improved SDR support

## Slide 9
OpenWebRX+ by Marat Fayzullin
OpenWebRX+
Marat Fayzullin forked OpenWebRX into OpenWebRX+ and added lots of decoding capabilities
Enhanced map (OSM) and filters
Lots of additional decoders (SSTV, AIS, CW, Page, Fax, ISM, HFDL/ACARS/ADS-B)
Enhanced Controls and Functions (NR, Rec, spectrum display)
File viewer for received SSTV pics

## Slide 10
OpenWebRX(+) Features
A walk through OpenWebRX(+) features and decoding capabilities

## Slide 11
Receive Audio
OpenWebRX(+) can receive and demodulate narrowband (FM, AM, SSB, CW) and wideband (WFM, broadcast) transmissions
Receive and demodulate audio

## Slide 12
Receive Digital Voice
OpenWebRX(+) can receive and demodulate ham radio digital voice (DV) modes D-Star, C4FM/YSF, DMR, NXDN and M17
Requirements: DV modes that use the proprietary, patented AMBE codec require the use of a codec server plus a hardware AMBE decoder (such as ThumbDV)
Receive and decode digital voice

## Slide 13
Squelch Control
OpenWebRX(+) has a built in squelch function to mute noise and static based on signal strength
Mute noise and static

## Slide 14
Waterfall controls
The waterfall display in OpenWebRX(+) is controllable via multiple slider controls and buttons
Setup display and bandwidth

## Slide 15
Receive Profiles
OpenWebRX(+) supports the simultaneous use of many SDRs and bands – just choose device and band via the profile dropdown box
Choose device and band

## Slide 16
Map view
OpenWebRX(+) has an integrated map view using Google maps or OpenStreetMaps to show positions of received stations (e.g. FT8 or APRS/Packet decodes)
Map

## Slide 17
Received Files
OpenWebRX+ has an integrated file viewer for received SSTV pictures
Received Files

## Slide 18
Audio Recorder
OpenWebRX+ supports live recording of received transmissions to a local .mp3 file using browser-based functions
Record Audio

## Slide 19
Noise Reduction
OpenWebRX+ supports configurable noise reduction on the received signals
Noise Reduction

## Slide 20
cw decoder
OpenWebRX+ has an integrated cw decoder
cw

## Slide 21
Digimodes: FT8
OpenWebRX(+) supports realtime FT8 decoding. Spots are shown on the internal map and uploaded to pskreporter
FT8

## Slide 22
Digimodes: FT4
OpenWebRX(+) supports realtime FT4 decoding. Spots are shown on the internal map and uploaded to pskreporter
FT4

## Slide 23
Digimodes: JS8Call
OpenWebRX(+) supports realtime JS8Call decoding. Spots are shown on the internal map and uploaded to pskreporter
JS8Call

## Slide 24
Digimodes: WSPR
OpenWebRX(+) supports realtime WSPR decoding. Spots are shown on the internal map and uploaded to wsprnet.org
WSPR

## Slide 25
Digimodes: BPSK31
OpenWebRX(+) supports realtime BPSK31 decoding. Decoded text is shown in the receiver panel
BPSK31

## Slide 26
Digimodes: SSTV
OpenWebRX+ supports realtime SSTV decoding. Received images are shown on the “Files” subpage
SSTV

## Slide 27
Digimodes: Packet(I)
OpenWebRX(+) supports realtime APRS AFSK 1K2 decoding. Received stations are shown on the internal map and uploaded to aprs-is
AFSK 1K2

## Slide 28
Digimodes: Packet(II)
OpenWebRX(+) supports a map view of received APRS stations
AFSK 1K2

## Slide 29
Digimodes: AIS(I)
OpenWebRX+ supports realtime AIS decoding. Received stations are shown on the internal map
AIS

## Slide 30
Digimodes: AIS(II)
OpenWebRX+ supports a map view of received AIS stations
AIS

## Slide 31
Digimodes: ADSB(I)
OpenWebRX+ supports realtime ADSB decoding. Received stations are shown on the internal map
ADSB

## Slide 32
Digimodes: ADSB(II)
OpenWebRX+ supports a map view of received ADSB stations
ADSB

## Slide 33
Digimodes: VDL2/ACARS
OpenWebRX+ supports realtime VDL2/ACARS and HFDL decoding on VHF airband. Decoded messages are shown in the receiver panel
VDL2/ACARS

## Slide 34
Digimodes: HFDL
OpenWebRX+ supports realtime HFDL decoding on 13MHz airband. Decoded messages are shown in the receiver panel
HFDL

## Slide 35
Digimodes: ISM
OpenWebRX+ supports realtime ISM band decoding on 433 MHz. Decoded messages are shown in the receiver panel
ISM

## Slide 36
Digimodes: FAX
OpenWebRX+ supports realtime FAX decoding. Decoded images are shown in the receiver panel and are accessible via “Files”
FAX

## Slide 37
Digimodes
MSK144
RTTY
JT65
JT9
FST4 / FST4W
Q65
Pagers
SelCall / ZVEI
Additional Digimodes are supported

## Slide 38
Map: Repeaters
OpenWebRX+ supports a map view of nearby repeaters (via repeaterbook)
Repeaters

## Slide 39
Map: WebSDRs
OpenWebRX+ supports a map view of WebSDRs: KiwiSDR, WebSDR, OpenWebRX
WebSDRs

## Slide 40
Settings Gui
OpenWebRX(+) has an integrated Web-based settings editor that enables easy configuration of station settings, SDR devices and profiles as well as decoding settings
Settings

## Slide 41
OpenWebRX(+) Deployment
How to roll your own instance of OpenWebRX(+)

## Slide 42
OpenWebRX(+) platform options
Docker container
There are readily built Docker containers for both OpenWebRX and OpenWebRX+, usable on any kind of platform (PC, VM, SBC)
Standard PC
Just use Linux (Debian, Ubuntu) and install OpenWebRX(+) packages
Virtual Machine
Same as PC, just using a Linux virtual machine w/ SDRs by USB passthrough or network
Single Board Computer (SBC)
SBCs like RaspberryPi or OrangePi can be used. There are readily built RasPi images for OpenWebRX and OpenWebRX+ for an easy, quick start

## Slide 43
Raspberry Pi 4B
As of Q4/2023, the gold-standard of single board computers
Good starting point for OpenWebRX(+)
Ready built images are available
Powerful enough for 1-2 SDRs and a small amount of users
priced at ~50,-€ incl. tax

## Slide 44
ODROID N2(+)
As of Q4/2023, still one of the most powerful single board computers (though it was released 2019)
No readily built image available, but docker ARM64 build can be used
2 – 2.5 times the performance of Raspberry Pi 4B
priced at ~100,-€ incl. tax

## Slide 45
Orange Pi 5
As of Q4/2023, one of the most powerful single board computers
No readily built image available, but docker ARM64 build can be used
2 – 2.5 times the power of odroid N2+
3.5 – 4 times the performance of RasPi 4B
Even more powerful that brand-new RasPi 5 (no details yet)
priced at ~100,-€ + tax

## Slide 46
Raspberry Pi 5
RTM Q4/2023, the gold standard in single board computers is getting a massive upgrade
Perfect starting point for OpenWebRX(+)
Ready built images are available
Performance should at level of ODROID N2+
priced at ~80,-€ incl. tax

## Slide 47
RaspberryPi install

## Slide 48
Package install
Manual installation via packages (as root)
wget -O - https://luarvique.github.io/ppa/openwebrx-plus.gpg | gpg --dearmor -o /etc/apt/trusted.gpg.d/openwebrx-plus.gpg
echo "deb [signed-by=/etc/apt/trusted.gpg.d/openwebrx-plus.gpg] https://luarvique.github.io/ppa/ubuntu ./" > /etc/apt/sources.list.d/openwebrx-plus.list
apt update
wget -O - https://repo.openwebrx.de/debian/key.gpg.txt | gpg --dearmor -o /usr/share/keyrings/openwebrx.gpg
echo "deb [signed-by=/usr/share/keyrings/openwebrx.gpg] https://repo.openwebrx.de/ubuntu/ jammy main" > /etc/apt/sources.list.d/openwebrx.list
apt update
apt install openwebrx

## Slide 49
Docker install

## Slide 50
OpenWebRX+ Demo

## Slide 51
OpenWebRX(+) Links
Project Websites
SDRs
Receiver Lists
Community
How to find public WebSDRs
Receiverbook: https://www.receiverbook.de/
Public KiwiSDRs: http://kiwisdr.com/public/
Public WebSDRs
http://websdr.org/
Contact authors and other OpenWebRX users
OpenWebRX Group: https://groups.io/g/openwebrx
OpenWebRX(+) Telegram chat: https://t.me/openwebrx_chat
Central source of information
OpenWebRX:
https://openwebrx.de/
https://github.com/jketterl/openwebrx/wiki
OpenWebRX+: https://github.com/luarvique/ppa
SDRs usable with OpenWebRX(+)
Airspy: https://airspy.com/
RTLSDR: https://www.nooelec.com/store/sdr.html
https://www.rtl-sdr.com/v4/
SDRplay: https://www.sdrplay.com/
HackRF
https://greatscottgadgets.com/hackrf/
PlutoSDR (Analog Adalm Pluto):
https://www.mouser.de/new/analog-devices/adi-adalm-pluto/
…

## Slide 52
Thanks for watching!
And now…
get started!